## Slide 1: One-balance model and KPIs

## Slide 2: Imbalance settlement framework development
In December 2017 EU commission established a guideline on electricity balancing in order to develop and harmonize European electricity markets
  The major changes concern the imbalance settlement period, the calculation of imbalance and the pricing of imbalance
The imbalance settlement period will change from hour to 15 minutes
The imbalance calculation will change in a way that there won’t be a separate production and consumption imbalances
  Two imbalances are replaced by a single imbalance
  One-balance model makes imbalance settlement more straightforward
The new pricing model will have same price for positive and negative imbalances during normal situation
  In specific conditions a dual pricing will be applied

## Slide 3: Current imbalance settlement model
consumption
planned production
px and bilateral trades
consumption imbalance adjustments
MGA imbalance
consumption imbalance power
production
planned production
production imbalance adjustments
production imbalance power
Consumption
Production
one-price model
two-price model

## Slide 4: Future imbalance settlement model
consumption
production
px and bilateral trades
imbalance adjustments
MGA imbalance
imbalance power
Consumption and production
single price model
* pricing of the imbalances is not yet agreed. Assumption is that there will be single price model but dual pricing will be used in certain ISPs.
From Two balance to One balance
Production plans are no longer included in the imbalance settlement

## Slide 5: Timetable for imbalance settlement development
2019
2020
2021
2022
2023
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
ONE BALANCE MODEL IMPLEMENTATION
15 MIN ISP IMPLEMENTATION
Go-live Q2/2021*
Go-live Q4/2022**
Detailed design of imbalance settlement model
*Schedule is based on an assumption in which dual imbalance price model can be applied on ISPs with divergent balancing directions. If it’s not possible to find a methodology with dual pricing in certain ISPs, the implementation of single pricing may be delayed until the introduction of 15 min ISP.
Q2/2020 Implementation plan will be presented to customer committee
**TSO proposal

## Slide 6: KPIs in one balance model
eSett has been publishing Key Performance Indicators (KPI) and advanced settlement reports for BRPs since the beginning of year 2019
Advanced settlement reports offers statistics and graphs to review performance and identify potential issues
BRP imbalance KPI report provides data for benchmarking and general information about the performance of BRPs
One Balance model combines the two separate BRP imbalances
  All KPIs need adjustment for the new model
  Formulas are kept reasonably similar

## Slide 7: Imbalance Result
Currently, Consumption Imbalance Result and Production Imbalance Loss are calculated:
  Consumption Imbalance Result
  Production Imbalance Loss
eSett Consumption Imbalance Purchase Quantity
Day-ahead Price
Consumption Imbalance Price
eSett Consumption Imbalance Sales Quantity
eSett Production Imbalance Sales Quantity
Day-ahead Price
Consumption Imbalance Price
eSett Production Imbalance Purchase Quantity

## Slide 8: Imbalance Result
New formula is “Imbalance Result” which simply replaces Consumption Imbalance Result
  Imbalance Result:
  Production Imbalance Loss will be discontinued
    Production imbalance is no longer calculated
eSett Imbalance Purchase Quantity
Day-ahead Price
Imbalance Price
eSett Imbalance Sales Quantity

## Slide 9: Imbalance Factor
Current formulas:
  Consumption Imbalance Factor
  Production Imbalance Factor
eSett Consumption Imbalance Sales Quantity eSett Consumption Imbalance Purchase Quantity
eSett Consumption Imbalance Purchase Quantity eSett Consumption Imbalance Sales Quantity
IF
THEN
ELSE
eSett Consumption Imbalance Purchase Quantity > eSett Consumption Imbalance Sales Quantity
eSett Production Imbalance Sales Quantity eSett Production Imbalance Purchase Quantity
eSett Production Imbalance Purchase Quantity eSett Production Imbalance Sales Quantity
IF
THEN
ELSE
eSett Production Imbalance Purchase Quantity > eSett Production Imbalance Sales Quantity

## Slide 10: Imbalance Factor
New “Imbalance Factor” only adjusts terms to One Balance:
Imbalance Skewness will also utilise One Balance terms:
    Currently, min / max thresholds are 0,4 / 2,5
eSett Imbalance Sales Quantity eSett Imbalance Purchase Quantity
eSett Imbalance Purchase Quantity eSett Imbalance Sales Quantity
IF
THEN
ELSE
eSett Imbalance Purchase Quantity > eSett Imbalance Sales Quantity
eSett Imbalance Sales Quantity eSett Imbalance Purchase Quantity

## Slide 11: Relative Imbalance
Currently, Relative Consumption Imbalance and Relative Production Imbalance are used:
  Relative Consumption Imbalance
  Relative Production Imbalance
Absolute Consumption Imbalance Quantity
Production Plan
Purchases
Minor Production
Absolute Production Imbalance Quantity
Normal Production

## Slide 12: Relative Imbalance
New formula “Relative Imbalance” follows the format of Relative Consumption Imbalance, except denominator term is calculated with consumption and total sales
Relative Imbalance:
  For a BRP who is not a power producer the results will almost identical to relative consumption imbalance
Relative Production Imbalance will be discontinued
  Production plan KPI
Sales
Absolute Imbalance Quantity
Consumption

## Slide 13: Production Plan KPI
As production plan is removed from imbalance calculations, a report for BRP is offered where they can see their production plan performance.
  KPI metric for aggregated values per MBA per PU type (solar etc.):
  BRP can see their own performance in Online Service reports
Production(MBA, type)
Production Plan
(MBA, type)
Production Plan
(MBA, type)
Imbalance Adj. down (MBA, type)
Imbalance Adj. up (MBA, type)
Imbalance Adj. up
(MBA, type)
Imbalance Adj. down (MBA, type)

## Slide 14: Advanced Settlement Report (Week/Month) changes
Current
New
Old charts will be removed, and new charts will replace them

## Slide 15: BRP Imbalance KPI Report (Own Data/Country) changes
Current
New

## Slide 16: BRP Imbalance KPI Report new formula
Current
New
Current

## Slide 17: BRP Imbalance KPI Report threshold values
Current
New